## Slide 1: Application of high-throughput molecular biology technologies to biological processes for biodegradation & bioenergy production from wastewater
Christopher M. Sales
Drexel University
March 12, 2013

## Slide 2: The Amazing Microbial World
“The role of the infinitely small in nature is infinitely large.” – Louis Pasteur

## Slide 3: Microbes, Humans, and the Environment
Since the late 1800s, environmental engineers have been harnessing the catalytic potential of microbes to protect the health of humans and the environment.
Activated Sludge Process
Anaerobic Digesters
Algae Photobioreactors
In situ soil bioremediation
High BOD
Low BOD
Organic Waste
CH4
Hazardous Contaminant
Benign Product
CO2
Lipid-rich Algae

## Slide 4: “Black Box” Approach to Biological Processes
Application of reactor theory and chemical kinetics are powerful tools for engineering biological processes…
Activated Sludge Process
Anaerobic Digesters
Algae Photobioreactors
In situ soil bioremediation
High BOD
Low BOD
Organic Waste
CH4
Hazardous Contaminant
Benign Product
CO2
Lipid-rich Algae
Reactants
(substrates)
Products

## Slide 5: “Black Box” Approach to Biological Processes
…however, the “black box” approach limits our understanding of the underlying microbial systems, and thus our ability to engineer them…
Reactants
(substrates)
Products

## Slide 6: Peeling back the “Black Box’’
Advances in high-throughput molecular and analytical techniques provide tools to shed light on complex microbial systems
Reactants
(substrates)
Products

## Slide 7: Central Dogma of Molecular Biology
Biodegradation and biosynthesis processes are catalyzed by enzymes!
DNA
(genes)
RNA
(transcripts)
Proteins
(enzymes)
Replication
Transcription
Translation
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 8: Era of “omes” and “omics”
Advances in high throughput techniques, such as next generation sequencing technologies, enable the study of “everything” in microbiology.
DNA
(genes)
genomes
METAGENOMES
single genes
all genes of an organism
all genes of a microbial community
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 9: Era of “omes” and “omics”
DNA
(genes)
RNA
(transcripts)
Proteins
(enzymes)
genomes
transcriptomes
proteomes
METAGENOMES
METATRANSCRIPTOMES
METAPROTEOMES
Metabolites
metabolome
METAMETABOLOME
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 10: Application of “omics” to Environmental Engineering
“Omics” technologies provide tools for a systems biology approach to study the complex interactions that are central to the physiology and function of environmental biological processes
Reactants
(substrates)
Products

## Slide 11: Application of “omics” to Environmental Engineering
“Omics” technologies provide tools for a systems biology approach to study the complex interactions that are central to the physiology and function of environmental biological processes
Reactants
(substrates)
Products

## Slide 12: APPLICATION OF “OMICS” TO 1,4-DIOXANE BIODEGRADATION

## Slide 13: Acknowledgements
UC Berkeley
Lisa Alvarez-Cohen
Ariel Grostern (Post-doc)
Weiqin Zhuang (Post-doc)
UCLA
Shaily Mahendra
UC Davis
Becky Parales
Juan Parales
UW-Madison
Jonathan Klassen (Post-doc)
Washington University in St. Louis
Yinjie Tang

## Slide 14: Emerging contaminant: 1,4-dioxane
Health Concerns
Confirmed animal carcinogen
Probable human carcinogen (Class B2)
Toxicities to kidney, liver, lungs, nasal cavity, and gall bladder
Cases of fatal occupational exposure (inhalation)

## Slide 15: Emerging contaminant: 1,4-dioxane
Sources
Primary Care Products (shampoos and cosmetics), as a byproduct of ethoxylation reaction
Stabilizer in 1,1,1-trichloroethane (1,1,1-TCA), a.k.a. methyl chloroform
Solvent in paper and textile processes, such as dialysis filters

## Slide 16: Emerging contaminant: 1,4-dioxane
Environmental concerns
High Solubility  Large Plumes
No Federal MCL
On the USEPA 3rd Contaminant Candidate List (CCL)
Demonstration of degradation by advanced oxidation processes and … Fungi and Bacteria!
From Environmental Sciences Division, Washenaw County, MI
1,4-dioxane contamination
in groundwater
up to 212,000 ug/L
(Fotouhi et al., 2006)
3 ug/L
Notification Level

## Slide 17: Biodegradation of 1,4-dioxane
Background
Pure and mixed cultures of fungi and bacteria primarily degrade 1,4-dioxane aerobically
Mainly co-metabolic degradation (i.e., need an inducing substrate for growth and to promote degradation)
To date, can be metabolized as carbon and energy source by only 9 isolates
Biochemical evidence for the involvement of monooxygenase (MO) enzymes in aerobic biodegradation of 1,4-dioxane [i.e., methane MO, propane MO, toluene MO, tetrahydrofuran (THF) MO]

## Slide 18: Pseudonocardia dioxanivorans CB1190
(a.k.a, strain CB1190)
Isolated from 1,4-dioxane contaminated sludge (South Carolina)
Gram-positive actinomycete
Grows on 1,4-dioxane and other ethers, including another cyclic ether tetrahydrofuran (THF)
Ability to fix CO2
Ability to fix N2
References: Parales et al., (1994) AEM; Mahendra & Alvarez-Cohen (2005) IJSEM

## Slide 19: Proposed metabolic pathway
1,4-dioxane degradation pathway
(Mahendra et al., 2007, ES&T)
Strain CB1190
Based on detected in-vivo intermediates using ESI-MS and FTICR-MS
Mineralization and incorporation into biomass confirmed by 14C-tracer study
However, enzymes are unknown!

## Slide 20: Functional genomics approach
DNA
(genes)
RNA
(transcripts)
Proteins
(enzymes)
Replication
Transcription
Translation
Use genome of strain CB1190 to identify the enzymes involved in 1,4-dioxane metabolism.
genomes
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 21: Genomic Sequencing at JGI
P. dioxanivorans CB1190
Isolation of
genomic DNA
Whole-genome shotgun sequencing
Genome Map
Alignment, assembly and annotation

## Slide 22: Pseudonocardia dioxanivorans CB1190 Genome
Genome consists of four genetic elements:
chromosome
3 plasmids
Feature | Genome | Chromosome | Plasmid pPSED01 | Plasmid pPSED02 | Plasmid pPSED03
Topology |  | Circular | Circular | Circular | Linear
Length | 7,440,794 bp | 7,096,571 bp | 192,355 bp | 136,805 bp | 15,603 bp
G+C Content | 73.12% | 73.41% | 71.15% | 68.38% | 61.83%
Coding Density | 87.2% | 88.5% | 76.1% | 80.0% | 69.2%
Coding Sequences | 6,797 | 6,495 | 172 | 116 | 14
Pseudo genes | 226 | 194 | 20 | 11 | 0
Average CDS length | 963 bp | 967 bp | 946 bp | 851 bp | 744 bp
rRNAs | 3 | 3 |  |  | 
tRNAs | 47 | 47 |  |  | 
Hypothetical proteins | 1,842 | 1,692 | 88 | 51 | 11
From Sales et al. (2012). J. Bacteiol. and Sales et al. (2013) submitted

## Slide 23: Pseudonocardia dioxanivorans CB1190 genome
Search for monooxygenases
Strategy 1:
Keyword search for “monooxygenases”
Result → 84 genes annotated as MOs!
Strategy 2:
Sequence similarity search to subunits of multi-component monooxygenases
Propane MO (prmABCD)
Phenol MO (dmnLMNOP)
Toluene MO (tmoABCDE)
Result → 8 multicomponent MOs
Sequence
Structure
Function
CB1190 Chromosome

## Slide 24: CB1190 Monooxygenases
Eight multicomponent MOs
All located on chromosome, except THF MO (plasmid pSED02)
From Sales et al. (2012). J. Bacteiol. and Sales et al. (2013) submitted

## Slide 25: Application of Transcriptomics
DNA
(genes)
RNA
(transcripts)
Proteins
(enzymes)
Transcription
Translation
Problem: Which monooxygenase is involved in the hydroxylation of 1,4-dioxane?
Solution: Use transcriptomics!
genomes
transcriptomes
1,4-dioxane degradation activity
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 26: Transcriptomics of 1,4-dioxane biodegradation
Whole genome expression analysis of CB1190 grown on 1,4-dioxane and glycolate (intermediate) using microarrays
Extract nucleic acids
Isolate and purify total RNA
Synthesize cDNA
Label cDNA
Quantify in qPCR
Hybridize to microarray
Signal reading

## Slide 27: Transcriptomics of 1,4-dioxane biodegradation
Example of Transcriptomics Microarray Data Analysis
From microarray study of propane-enhanced bacterial degradation of the water contaminant N-nitrosodimethylamine (NDMA)
Microarray study described in Sharp, Sales et al. (2007). AEM.

## Slide 28: Transcriptomics of 1,4-dioxane biodegradation
Comparison of CB1190 grown on 1,4-dioxane vs. glycolate
Results:
383 genes were differentially expressed
  97 genes up-regulated on 1,4-dioxane
  286 genes down-regulated on 1,4-dioxane
The only MO up-regulated was the THF MO gene cluster (thmADBC) located on plasmid pPSED02
From Sales et al, (2013) submitted

## Slide 29: Revision of upper-portion of 1,4-dioxane pathway
Strain CB1190 genome was used to identify protein-encoding genes involved in upper pathway
Up-regulation of genes verified by transcriptomics further supported their involvement
From Grostern, Sales et al. (2012) AEM; Sales et al, (2013) submitted

## Slide 30: Metabolomics of 1,4-dioxane biodegradation
Uniformly 13C-labeled 1,4-dioxane tracer study
Unlabeled carbon indicated with an asterisk (*)
From Grostern, Sales et al. (2012). AEM.

## Slide 31: Revision of lower portion of 1,4-dioxane pathway
Heterologous expression of putative glyoxylate degradation genes in Rhodococcus jostii RHA1
Tartronate semialdehyde reductase, GlxR (3389)
Glyoxylate carboligase, Gcl (Psed_3890)
From Grostern, Sales et al. (2012). AEM.

## Slide 32: Revised pathway
Revised 1,4-dioxane biodegradation pathway annotated with enzymes, using genomics, transcriptomics, and metabolomics.
From Grostern, Sales et al. (2012). AEM.

## Slide 33: Closer look at upper pathway
Hydroxylation of 1,4-dioxane and HEAA
Is it the same or different MO?
  Genomics and transcriptomics studies not sufficient to verify involvement in both 1,4-dioxane and HEAA degradation
  Activity of THF MO on hydroxylation of 1,4-dioxane or 1,4-dioxane can only be confirmed by heterologous expression in another host of thm gene cluster or genetic deletion (knockout) from strain CB1190
?
1,4-dioxane
HEAA
2-hydroxyethoxyacetic acid

## Slide 34: Confirmation THF MO Functional Activity
Heterologous expression of thm genes
THF MO (thmADBC) was successfully expressed on a vector in the host Rhodoccocus jostii RHA1
Results indicate THF MO can hydroxylate 1,4-dioxane, but not HEAA
1,4-dioxane
HEAA
thmADBC
thmADBC
YES!
NO!
From Sales et al. (2013). In prep.

## Slide 35: Application of “Omics” to 1,4-dioxane biodegradation
Summary
Combination of approaches led to the identification of the genetic basis of 1,4-dioxane metabolism
  Microbiology, molecular biology, and biochemical methods
  High-throughput techniques (genomics, transcriptomics, metabolomics),
Determined and verified the involvement of THF MO in the hydroxylation of 1,4-dioxane
  Genetic biomarkers can now be designed to
    Identify the potential for 1,4-dioxane biodegradation at a contaminated site
    Monitor the gene expression of 1,4-dioxane-degrading enzymes during bioremediation efforts

## Slide 36
Water and Energy Nexus
Water
Energy
Biological Systems

## Slide 37: OPPORTUNITIES FOR USE OF HIGH-THROUGHPUT TECHNIQUES IN ENGINEERING WASTE-TO-ENERGY BIOTECHNOLOGIES

## Slide 38: Wastewater Treatment Plants (WWTPs)
Main goal is to protect natural water bodies by removal of
  oxygen-demanding substances in wastewater
  nitrogen and phosphorous compounds in wastewater
WWTPs…successful in removal, but in general, are wasteful…
Primary
Treatment
Secondary
Treatment
Tertiary
Treatment
Raw
Wastewater
(High Organics;
High NH3;
High P)
Treated
wastewater
(Low Organics;
Low NH3;
Low P)
CO2
O2
Waste Sludge
(Biomass)
N2
P-rich Sludge
(Biomass)
Image: EBMUD
Waste Sludge
(primary solids)

## Slide 39: Rethinking Wastewater Treatment
WWTPs as Sustainable Resource Recovery Plants
Recovery of water resource
Recovery of nutrients (e.g., N and P)
Recovery of biosolids for agricultural use
Recovery of energy from sludge or wastewater
Primary
Treatment
Secondary
Treatment
Tertiary
Treatment
Raw
Wastewater
(High Organics;
High NH3;
High P)
Treated
wastewater
(Low Organics;
Low NH3;
Low P)
CO2
O2
Waste Sludge
(Biomass)
N2
P-rich Sludge
(Biomass)
Energy
Source
Protein
Source
Energy
Source

## Slide 40: Waste-to-Energy Biotechnologies
Biological processes
Biogas production (anaerobic digesters)
Bioelectricity production (microbial fuel cells)
Biohydrogen production
Biofuel production (algal photobioreactors, fermenters)
Wastes
Energy

## Slide 41: Waste-to-Energy Biotechnologies
Application of high-throughput techniques (omics)
Metagenomics
  Discover novel organisms, enzymes, pathways
  Study the evolution (natural or adaptive) of microbial community structure and key functional genes
Metatranscriptomics
  Understand molecular and biochemical interactions regulating enzyme production (activity)
Meta-metabolomics
  Characterize key metabolic pathways
  Identification of rate-limiting biochemical reactions
  Examine exchange of nutrients and metabolites between organisms

## Slide 42: Final Remarks
“Omics” can be applied in combination with other methods to study environmental biological processes
“Omics” can provide insight into the microbial and molecular systems that control the function of environmental biological processes
“Omics” has the potential to revolutionize our approach to studying and engineering biological processes for environmental sustainability

## Slide 43: Questions?

## Slide 44: Additional Slides

## Slide 45: Shale Gas and Microorganisms
Potential areas of research related to environmental impacts of hydraulic fracturing and biological systems
Development of microbial source tracking methods for monitoring releases caused by hydraulic fracturing activity
Investigate the effects of high TDS, metals, and biocides in flow-back and processed waters from hydraulic fracturing on biological processes for wastewater treatment (i.e., activated sludge)
Study changes in microbial activity important to biogeochemical cycles (particularly carbon) in soils and sediments near shale oil and gas extraction sites

## Slide 46: Central Dogma of Molecular Biology
DNA
(genes)
RNA
(transcripts)
Proteins
(enzymes)
Replication
Transcription
Translation
Notes: Protein Image: http://xray.bmc.uu.se/~michiel/research.php

## Slide 47: Metabolic Pathways
Multiple enzyme reactions are required in metabolic pathways.
(e.g., citric acid cycle for metabolizing pyruvate into CO2)

## Slide 48: Chemical Properties
Property | 1,4-dioxane | NDMA
Molecular weight | 88.11 | 74.08
Density | 1.028 g/cm3 | 1.0059 g/cm3
Water solubility | Miscible | Miscible
Boiling point | 101.2⁰C | 154⁰C
Vapor pressure | 5.08 kPa at 25⁰C | 0.36 kPa at 25⁰C
Octanol-water partition coefficient (log Kow) | -0.27 | -0.57
Organic carbon partition coefficient (log Koc) | 1.23 | 1.079
Henry’s law constant (Hc) | 4.80 x 10-6 atm-m3/mol | 2.63 x 10-7 atm-m3/mol
Henry’s law constant (dimensionless, Hc*) | 1.96 x 10-4 | 1.1x10-5
a Sources: USEPA, 2010; Mohr et al., 2010 and references therein
b Sources: ATSDR, 1989; USEPA, 2008

## Slide 49: Genome Sequencing
http://www.scq.ubc.ca/genome-projects-uncovering-the-blueprints-of-biology/
Sanger Sequencing (1975)
Dye-based
Average sequence length: 800 bp
Method for producing draft of human genome (2001)
Human Genome: 3.4 Gb (billion bp)
Bacterial Genomes: ~ 1-10 Mb (million bp)
Applied Biosystems Inc.,
Capillary Electrophoresis
Sequencer

## Slide 50: Producing the Genome
Circular Genome Map

## Slide 51: Genomics
Circular Genome Map
Predict Function & Physiology

## Slide 52: Next Generation Sequencing (NGS)
http://www.ncbi.nlm.nih.gov/genbank/genbankstats-2008/
Human Genome (3.4 Gbp):
2000 - $15.3 billion (4.5x Coverage)
2012 - $3,400 (1000x Coverage)

## Slide 53: Next Generation Sequencing (NGS)
Sanger
800 bp
0.01 GB/run
454 Pyrosequencing
200-400bp
0.1-1 GB/run
Illumina/Solexa
GAI/GAII
25-50 bp
1-10 GB/run
Illumina HiSeq
100-200bp
100 GB/run
2000
2005
2010
Ion Torrent
Nanopore
200 bp
0.8GB/run
Pacific Biosciences
10,000 bp?
?GB/run
2013
Increasing speeds, Decreasing Costs
Variability in Errors/Accuracy

## Slide 54: CB1190 Genome Sequencing Statistics
Date Released | Technology | Library Type | Average Read Length (bp) | Number of Reads
June 2009 | 454 | Single reads | 250 | 472 000
June 2009 | 454 | Single reads | 380 | 702 000
June 2009 | 454 | 20 Kb mate-pair | 380 | 2 400
Oct. 2009 | 454 | 10 Kb mate-pair | 380 | 143 000
Oct. 2009 | Illumina | Single reads | 36 | 33 000 000
Feb. 2010 | 454 | 3 Kb mate-pair | 380 | 65 000

## Slide 55: Metabolomics
13C-Tracer Analysis
Labeled carbon substrate
13C1-C2-C3-C4-C5-C6
Intracellular fluxes
PP Pathway
Glycolysis
Metabolites
TCA Cycle
bio-products + biomass
Agilent 5973
mo
m1
m2
m3
Isotopomers
Adapted from Tang, 2007

## Slide 56: Cornerstone of bioinformatics
Exploit relationships among
Particularly, interested in how,
  Sequence similarity relates to homology
  Homology relates to the structure, function, and evolution of a protein
  Definition: Homology is the relationship of two sequences or structures that have descended from a common ancestor.
Sequence
Structure
Function

## Slide 57: Environmental Engineers & Bioinformatics
Environmental engineers can utilize bioinformatics tools
    to sort
    to manage
    to analyze
copious amounts of information that characterize complex
biological systems (e.g., wastewater treatment plants, wetlands, contaminated soils)…
…in order to monitor (or manipulate) the numbers and types of enzymes (or organisms) that influence the forms and rates of bioremediation.

## Slide 58: Up-regulation of Propane MO
Chart: Log Fold Change in Expression
| prmA | prmB | alkB
qPCR(Pfaffl) | 3.3888 | 3.4797 | 0.50693
Microarray | 2.0969 | -0.18709
Expression levels. White (□), RT-qPCR and gray (■) spotted microarray. No prmB probes on microarray.
From Sharp, Sales et al. (2007). AEM.

## Slide 59: Genetic Knockouts of MOs
Chart: Hours
| 0 | 0.91666666668606922 | 1.8333319444209337 | 2.8333333333139308 | 3.75 | 19.250000000058208
prmA_A1-1 KO | 200 | 182.7075 | 186.7843 | 212.4395 | 226.5809 | 203.617
alkB_B1-20 KO | 200 | 172.2766 | 168.1202 | 59.3047 | 0 | 0
wildtype | 200 | 174.1399 | 155.9695 | 27.3592 | 0 | 0
abiotic | 186.5773 | 197.6611 | 246.7419 | 206.8976 | 162.1802
Where □ = wild-type RHA1; ▲ = knockout mutant RHA1ΔalkB; ◊ = knockout mutant RHA1ΔprmA; and ● = no cell control. Cells were grown in LB medium and harvested in the late exponential phase of growth. 200 mg NDMA-1 was added to each sample and NDMA monitored over time. Error bars portray the mean deviation of biological replicates.
From Sharp, Sales et al. (2007). AEM.

## Slide 60: Biomarkers for Propane MOs
Made oligonucleotide primers for PCR (PrMO Biomarker)
Based on multiple sequence alignment of known propane MO sequences
Expect PCR amplicon of 1400 bp
Primer only positive for Rhodococcus jostii RHA1 and Rhodococcus RR1 (not Mycobacterium vaccae JOB5)
Can be used to make predictions for in vivo bioremediation
From Sales et al. (2010). AEM.

## Slide 61: Omics guided NDMA degradation research
Summary:
Propane-enhanced, co-metabolic NDMA biodegradation is observed in RHA1 (like RR1)
Propane MO operon (prm) is up-regulated during growth on propane in RHA1 and RR1, but not JOB5
RHA1 prm genetic mutant unable to degrade NDMA