## Slide 1: Vacuum Oven Safety Presentation
Linfan Cui
lc944@drexel.edu
October 22, 2018

## Slide 2: Why use vacuum oven
For a variety of application of heat treatment under vacuum
For drying
For outgassing
For moisture removal.
For annealing
Materials
Thermo-sensitive
Easily oxidized

## Slide 3: Vacuum ovens in the lab
Observation window
Pump
Vacuum valve
Door handle
Vacuum gauge
Control panel
Purge valve

## Slide 4: Operating procedure
        Place sample inside of the oven. Make sure that the sample is mostly dry (i.e., there is no visible solvent present). If there are other samples in the oven place your samples away from them to prevent any contamination.
        Close the vacuum oven door. Check that the purge valve is closed, if not close it.
        Turn the pump on, open the vacuum valve slowly and turn off the pump when reaching vacuum. If the pressure gauge in front of the vacuum oven does not show the pressure going down, hold the vacuum oven door closed.
        Close the vacuum valve and slowly open the purge valve
        Take out your samples from the vacuum oven.
        Pump again to make sure the oven in a vacuum
Sample loading
Sample removing
        Notice: if you stop the vacuum pump at an evacuated state, the oil in the pump
        may flow backwards inside the oven.

## Slide 5: Best practice
Before use
In use
After use
Schedule time on the faces
Familiar with the procedure
Ask super-users
Wear lab coat, goggle and gloves
Follow the procedures
Use the logbook
Clean the oven
Inspect the oven
Make a note in the logbook

## Slide 6: Safety constrains
Do not use the unit in an area where
there is flammable or explosive gas
Always ground the unit
Do not touch heat parts
Do not disassemble and modify the oven

## Slide 7: Maintenance
        Don’t use corrosive samples
        Prevent pump oil flowing back-forward
        Don’t use the oil pump too long
        Let the oven being a vacuum after using it
        Notice the temperature range
        Keep the chamber clean
        Take care of the oven and your samples